## Slide 1: Introduction to Robotics CSE 461
Class Topic: Introduction to Control System Theory (PID)
Brac University

## Slide 2: 2nd order control system

## Slide 3: Effect of PID controller function

## Slide 4: Proportional works with football field

## Slide 7
Desired Altitude - Actual Altitude
= 60m - 0m
= 60

## Slide 8
Desired Altitude - Actual Altitude
= 60m - 0m
= 60
= Error

## Slide 10
Desired Altitude
Actual Altitude
Gain
Propeller
Altitude Measuring Sensor

## Slide 11
Desired Altitude
Actual Altitude
1
Propeller
Altitude Measuring Sensor

## Slide 12
Desired Altitude
Actual Altitude
1
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m - 0m
= 60
Propeller Speed = 60 * 1 = 60 rpm

## Slide 13
Desired Altitude
Actual Altitude
1
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m - 0m
= 60
Propeller Speed = 60 * 1 = 60 rpm

## Slide 14
Desired Altitude
Actual Altitude
2
Propeller
Altitude Measuring Sensor

## Slide 15
Desired Altitude
Actual Altitude
2
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m - 0m
= 60
Propeller Speed = 60 * 2 = 120 rpm

## Slide 16
Desired Altitude
Actual Altitude
2
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m - 5m
= 55
Propeller Speed = 55 * 2 = 110 rpm

## Slide 17
Desired Altitude
Actual Altitude
2
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m - 10m
= 50
Propeller Speed = 50 * 2 = 100 rpm
10m

## Slide 18
Desired Altitude
Actual Altitude
2
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m – 10.1111m
= 49.9999
Propeller Speed = 49.99 * 2 = 99.99 rpm
10m

## Slide 19
Desired Altitude
Actual Altitude
10
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m - 10m
= 50
Propeller Speed = 50 * 10 = 500 rpm
10m

## Slide 20
Desired Altitude
Actual Altitude
10
Propeller
Altitude Measuring Sensor
50m
Desired Altitude - Actual Altitude
= 60m - 50m
= 10
Propeller Speed = 10 * 10 = 100 rpm

## Slide 21
Desired Altitude
Actual Altitude
10
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m - 60m
= 0
Propeller Speed = 0 * 10 = 0 rpm

## Slide 22
Desired Altitude
Actual Altitude
100
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m - 59m
= 1
Propeller Speed = 1 *100 = 100 rpm

## Slide 23
Desired Altitude
Actual Altitude
10
Propeller
Altitude Measuring Sensor
Desired Altitude - Actual Altitude
= 60m – 59.1m
= .9
Propeller Speed = .9 * 10 = 90 rpm

## Slide 24
Desired Altitude
Actual Altitude
10
Propeller
Altitude Measuring Sensor
Propeller Speed = 10 * 10 = 100 rpm
Error = 10
50m
Output = Kp * error

## Slide 25
Desired Altitude
Actual Altitude
10
Propeller
Altitude Measuring Sensor
Propeller Speed = 10 * 10 = 100 rpm
Error = 10
50m
Output = Kp * error
Proportional Control

## Slide 26
Proportional Control
Steady-State error

## Slide 27: PID Controller

## Slide 29
Desired Altitude
Actual Altitude
Ki*e + Kp * ∫e
Propeller
Altitude Measuring Sensor
Propeller Speed = 10 * 10 = 100 rpm
Error = 10
50m

## Slide 30
Desired Altitude
Actual Altitude
Ki*e + Kp * ∫e
Propeller
Altitude Measuring Sensor
Propeller Speed = 10 * 10 = 100 rpm
Error = 10
50m
Output = Kp * error + Ki * (error1 + error2 +…+ errorN(0))
Proportional - Integral Control

## Slide 31
Desired Altitude
Actual Altitude
Kp*e + Ki * ∫e
Propeller
Altitude Measuring Sensor
Propeller Speed = 10 * 10 = 100 rpm
Error = 10
50m
Output = Kp * error + Ki * (error1 + error2 + … +errorn (0))
Output1= 10*60+5*60=900
Output2= 10*50+5(60+50)=1050
Output3= 10*40+5(60+50+40)=1150
Output4= 10*30+5(60+50+40+30)=1200
Output5= 10*20+5(60+50+40+30+20)=1200
Output6= 10*10+5(60+50+40+30+20+10)=1150
Output7= 10*0+5(60+50+40+30+20+10+0)=1050

## Slide 32
Desired Altitude
Actual Altitude
Ki*e + Kp * ∫e
Propeller
Altitude Measuring Sensor
50m

## Slide 33
Proportional Control

## Slide 34
Desired Altitude
Actual Altitude
Ki*e +
Kp * ∫e + Kd * ∇ e
Propeller
Altitude Measuring Sensor
Propeller Speed = 10 * 10 = 100 rpm
Error = 10
50m
Output = Kp * error + Ki * (error1 + error2 + error3) + Kd * ( error3- error 2)

## Slide 35
Desired Altitude
Actual Altitude
Ki*e +
Kp * ∫e + Kd * ∇ e
Propeller
Altitude Measuring Sensor
Propeller Speed = 10 * 10 = 100 rpm
Error = 10
50m
Output = Kp * error + Ki * (error1 + error2 + error3) + Kd * ( error3- error 2)
Proportional - Derivative - Integral Control
(PID) Control

## Slide 36
Desired Altitude
Actual Altitude
Ki*e +
Kp * ∫e + Kd * ∇ e
Propeller
Altitude Measuring Sensor
Propeller Speed = 10 * 10 = 100 rpm
Error = 10
50m
Output = Kp * error + Ki * (error1 + error2 + error3) + Kd * ( error3- error 2)
Output1= 10*60+5*60+.5*60=930
Output2= 10*50+5(60+50) +.5*(60-50)=1055
Output3= 10*40+5(60+50+40) + .5*(50-40)=1155
Output4= 10*30+5(60+50+40+30) + .5*(40-30)=1205
Output5= 10*20+5(60+50+40+30+20) + .5*(30-20)=1205
Output6= 10*10+5(60+50+40+30+20+10) + .5*(20-10)=1155
Output7= 10*0+5(60+50+40+30+20+10+0) + .5*(10-0)=1055

## Slide 37
Proportional - Derivative - Integral Control
(PID) Control

## Slide 38: Effect of Controller Functions
• Proportional Action
Simplest Controller Function, The P term helps to reduce the steady-state error and improve the system's responsiveness. However, too high of a proportional gain can lead to instability and oscillations in the system's response.
• Integral Action
Eliminates steady-state error, The I term helps to improve the system's stability and eliminate any bias in the system. However, too high of an integral gain can lead to overshoot and instability in the system's response.
• Derivative Action (“rate control”)
Effective in transient periods, The D term helps to improve the system's stability and reduce the effects of disturbances in the system. However, too high of a derivative gain can lead to noise amplification and instability in the system's response.

## Slide 40: Generating PID parameters
Auto-Tuning Algorithms:
  Relay-based Auto-Tuning
  A relay is introduced in the control loop.
  Observes the system's oscillatory response.
  Calculates PID parameters based on oscillation characteristics.
Trial and Error: Iteratively adjust parameters based on system response.

## Slide 41: Advantages and Applications of PID control
Advantages:
Simple: easy to understand.
Effective: Accurate and stable, even in dynamic environments.
Robust: Can be adopted to different robot systems
Application:
Arm positioning
Robot Navigation
Speed Control
Balance control

## Slide 42: Next Class
Machine Learning